# IPv6
IPv6 is the most recent version of the IP protocol an important change from IPv4 is that IPv6 uses 128-bits for address space instead of the 32-bit address space of IPv4. This is important since the IPv4 address pool is all but exhausted. IPv4 provides about 4.29 billion addresses which means that far from every person on earth can have a device with an IPv4 address.
## IPv6 headers
The IPv6 header is simpler than that of IPv4 which allows for faster processing. The IPv6 header is fixed in size at 40 bytes (the IPv4 header has a maximum size of 60 bytes) and includes options as extension headers that are only there when actually used. This makes the design easier to extend for future additions.
1 byte	1 byte	1 byte	1 byte
Version	Traffic Class	Flow Label
Payload length		Next Header	Hop Limit
Source Address
Destination Address

Illustration 1: The IPv6 fixed header format.
Referring to Illustration 1 above this is a description of the header fields:
- Version: Protocol version number = 6.
- Traffic Class: The 6 most-significant bits are used fto classify packets. The remaining 2 bits are used in order to signal impending congestion.
- Flow Label: Used to label sequences of packages that are to be treated the same way by allowing for more efficient processing by routers.
- Payload Length: Length of the payload limited to 64K y the size of this field. IPv6 can use an extension called Jumbo frames to send larger payloads. The length counts everything after the fixed header, included the extension headers.
- Next Header:
  - If the next header is UDP or TCP, this field will contain the same protocol numbers as in IPv4, for example, protocol number 6 for TCP or 17 for UDP. The protocol numbers are available through IANA at https://www.iana.org/assignments/protocol-numbers/
  - If extension headers are used, this is the type of the next extension header.
- Hop Limit: Decremented by 1 by each node that forwards the packet. The packet is discarded if Hop Limit is decremented to zero.
- Source Address: 128-bit address of the source of the packet.
- Destination Address: 128-bit address of the intended recipient of the packet, this might be the ultimate recipient if a Routing header is present.
Below is an illustration of the extension headers and payloads organisation, coming after the fixed IPv6 header.
Fixed header	Extension header 1	Extension header ...	Extension header N	Payload

Illustration 2: IPv6 fixed, and extension -header followed by the payload.
## IPv6 addressing
IPv6 addresses are either unicast, anycast, or multicast addresses
- Unicast addresses identify a single network interface and the IP packages will be sent to that interface.
- Anycast addresses are assigned to a group of interfaces. Anycast addresses has the same format as unicast addresses and differ only by the fact that they are present on more than one interface in the network. An anycast packet is delivered to one member, typically the nearest host according to the routing protocols definition.
- Multicast addresses are assigned to a group of interfaces, each member processes a message send to a multicast address.
An IPv6 address has 128 bits and address is divided into eight 16-bit hexadecimal blocks
separated by colons. For example:
2001:0DB8:0000:0000:00C0:FEFE:BADA:5500
There are some rules for shortening addresses like this:
- Leading zeroes can be skipped.
  - 2001:DB8:0:0:C0:FEFE:BADA:5500
- A double colon can replace a string of consecutive zeroes in more than one 16-bit address block, but a double colon can only be used once in the address
  - 2001.DB8::C0:FEFE:BADA:5500
Because of the transition from IPv4 to IPv6, still in progress, a special syntax has been introduced where the least 32 bits of an address can be written in the familiar dot notation of IPv4:
::ffff:c000:0280 and ::ffff:192.0.2.128 is the same, but the second form will be more recognisable if you have ever worked with IPv4.
### Special addresses
- ::/127 – Is for point to point connections like the IPv4 /30 prefix. In IPv6 there is no need for the broadcast and network address.
- ::/128 – The unspecified address that corresponds to the IPv4 0.0.0..0/32 address. This address must never be assigned to an interface, but is for instance used to get software to listen for incoming connections on all interfaces
::/0 - The default route address that corresponds to the IPv4 0.0.0.0/0 in IPv4.
- ::1/128 – The loopback address.
- fe80::/10 – This is a link-local address and compares to the auto-configuration type address of IPv4. The last 64 bits are usually chosen as the interface hardware address in modified EUI-64 format, basically adding ff:ee in the middle of the 48-bit MAC address. Addresses in the link-local prefix are only valid and unique on a single link.
fc00::/7 - Unique local addresses (ULAs), these addresses are comparable to IPv4 private addresses (10.0.0.0/8, 172.16.0.0/12 and 192.168.0.0/16). Like their IPv4 counterparts they are routable only within a set of cooperating sites. There are provisions in this range for doing addresses that will most likely not clash when merging more networks.
- ::ffff:0:0/96 - This prefix is designated as an IPv4-mapped IPv6 address.
- 64:ff9b::/96 - Addresses with this prefix are used for automatic IPv4/IPv6 translation.
2002::/16 - This prefix is used for 6to4 addressing.
2001::/32 — Used for Teredo tunneling, a transition technology that gives full IPv6 connectivity for IPv6-capable hosts that are on the IPv4 Internet, it functions from behind NAT devices.
2001:db8::/32 — This prefix is used in documentation.

## Juniper configuration.
(The full configuration is in the appendix)
This is a basic configuration setting IPv6 addresses on a logical tunnel.
interfaces {
    lt-0/0/0 {
        #vSRX-1
        unit 11 {
        encapsulation ethernet;
        peer-unit 21;
The inet6 family tells the SRX to use the inet6 routing table.
        family inet6 {
        address fdaa:dead:beef:1::1/127;
        }
        }
        #vSRX-2
        unit 21 {
        encapsulation ethernet;
        peer-unit 11;
        family inet6 {
        address fdaa:dead:beef:1::1/127;
        }
        }
    }
## Sources:
Wikipedia - Open Shortest Path First - https://en.wikipedia.org/wiki/Open_Shortest_Path_First
The Internet Engineering Task Force – RFC2460 - https://tools.ietf.org/html/rfc2460
IANA – Protocol numbers - https://www.iana.org/assignments/protocol-numbers/protocol-numbers.xhtml
EAL - IPv6 Essentials Addressing