OSPF (all of configurations are located in Appendix)
OSPF is short for Open Shortest Path First and is the name of a routing protocol. OSPF is an interior gateway protocol which means that it is used to exchange routing information within an autonomous system.

Routing Policy allows user to control the flow of routing information between the routing protocols and the routing tables and between the routing tables and the forwarding table. Routing policy allows you to control which routes the routing protocols store in and retrieve from the routing table.

Routing policy was used because:
- It was not an intention to import all routes into routing table. Routes were specified by proper match criteria in terms.
- According to route redistribution It was intended to transfer active routes learned from another routing protocol (BGP/OSPF, IS-IS/OSPF)

Routing Policy Flow:

Number of terms in routing policy is equal or bigger than 0, the software evaluates terms until it reaches a terminating action or end policy. Names of policies and terms are defined by user.
Each term contains “from” and “then” statement. The first describe match condition(s) and the second one describe action that is taken if a “from” statement is matched.

Match criteria that was used in project:
- from protocol direct
- from protocol ospf
- route-filters (192.168.0.0/22 longer; 10.0.0.44/30 exact; 10.0.0.36/30 exact)
“from” statement describes match conditions
Match types used in project: longer, exact.
- Exact match the specified prefix and mask exactly (10.0.0.36/30 exact)
- Longer match routes that have longer masks (192.168.0.0/22 longer)

Actions
“then” statement describes the actions to take if a “from” statement is matched.
Just one terminating action was used in project, it was “accept”

Implementing Routing Policy.
Defined routing policy is always located under the [edit policy-options] hierarchy on Juniper Device. (configuration in Appendix)
Quick set-up:
[edit policy-options]
set policy-options policy statement ospf-isis term 1 from protocol ospf
set policy-options policy statement ospf-isis term 1 from route-filter 192.168.0.0/22 longer
set policy-options policy statement ospf-isis term 1 then accept

policy-options {
	policy-statement ospf-isis {
	term 1 {
	from {
	protocol ospf;
	route-filter 192.168.0.0/22 longer;
	}
	then accept;
	}
	}

Applied routing policies as import or export policies can be found at different hierarchy levels (for example under routing-instances or protocols)

[edit protocols]
set isis export ospf-isis
set isis interface ge-0/0/7.0
set isis interface lo0.0
protocols {
	isis {
	export [ ospf-isis send-direct-to-isis-neighbors ];
	interface ge-0/0/7.0;
	interface lo0.0;
	}

Sources:
Routing Policy presentation
https://www.juniper.net/documentation/en_US/junos/information-products/pathway-pages/config-guide-policy/config-guide-policy.html