# Route Re-distribution OSPF/IS-IS
This chapter is about re-distributing OSPF to IS-IS and visa verse. Since each routing protocol has its own chapter this is mainly summarising the configuration on the Juniper SRX series router.

## Configuring the Juniper SRX
(The full configuration is available in the appendix)

Illustration 1: The network diagram of the network where OSPF - IS-IS redistrubution is configured
The OSPF router has a standard OSPF configuration but the loopback interface has multiple addresses used to simulate routing destinations.

Interfaces {

The ge-0/0/9 interface is connected to the router doing redistribution.
    ge-0/0/9 {
        unit 0 {
        family inet {
        address 10.0.0.46/30;
        }
        }
    }

The lo0 interface is configured to have several addresses to simulate route destinations.

    lo0 {
        unit 0 {
        family inet {
        address 192.168.1.1/32;
        address 192.168.2.1/32;
        address 192.168.3.1/32;
        address 192.168.0.1/32;
        }
        }
    }
}

Packages to the simulated destination are discarded.

routing-options {
    static {
        route 192.168.0.0/24 discard;
        route 192.168.1.0/24 discard;
        route 192.168.2.0/24 discard;
        route 192.168.3.0/24 discard;
    }
    autonomous-system 22;
}

The loopback interface and the interface connected to the IS-IS router is added to OSPF area 1 and the static routes are exported into OSPF using the “ospf” policy.

protocols {
    ospf {
        export ospf;
        area 0.0.0.1 {
        interface ge-0/0/9.0;
        interface lo0.0 {
        passive;
        }
        }
    }
}

policy-options {
    policy-statement ospf {
        term 1 {
        from protocol static;
        then accept;
        }
    }
}
security {
    forwarding-options {
        family {
        mpls {
        mode packet-based;
        }
        }
    }
}

The router that does redistributiuon has both OSPF and IS-IS configured on it.

interfaces {

The first interface connected to the router running OSPF configured above.

    ge-0/0/5 {
        unit 0 {
        family inet {
        address 10.0.0.45/30;
        }
        }
    }

These interfaces connects the router doing OSPF/IS-IS redistribution (ge-0/0/6), the routing instance that does IS-IS shown at the far left side of the network diagram. Notice that “family iso” is included as described in the IS-IS chapter.

    ge-0/0/6 {
        unit 0 {
        family inet {
        address 10.0.0.38/30;
        }
        family iso;
        }
    }
    ge-0/0/7 {
        unit 0 {
        family inet {
        address 10.0.0.37/30;
        }
        family iso;
        }
    }
Set the routers ISO addresses on the loopback interface. The router is in a private area (49) with an ID of 2. The redistributing router has an system id of 0172.0016.0907 and the pure IS-IS router has an ID of 0172.0016.0305.

    lo0 {
        unit 0 {
        family inet {
        address 176.16.1.2/32;
        }
        family iso {
        address 49.0002.0172.0016.0907.00;
        }
        }
        unit 1 {
        family inet {
        address 172.16.3.5/32;
        }
        family iso {
        address 49.0002.0172.0016.0305.00;
        }
        }
    }
}

All routers are in AS17.

routing-options {
    autonomous-system 17;
}

Allow export of IS-IS into OSPF and OSPF into the IS-IS and allow the IS-IS routers to talk to each other.

protocols {
    isis {
        export [ ospf-isis send-direct-to-isis-neighbors ];
        interface ge-0/0/7.0;
        interface lo0.0;
    }
    ospf {
        export send-direct-to-ospf-neighbors;
        area 0.0.0.1 {
        interface ge-0/0/5.0;
        interface lo0.0 {
        passive;
        }
        }
    }
}
policy-options {

Allow traffic from the dummy routing destinations set up in the OSPF router.

    policy-statement ospf-isis {
        term 1 {
        from {
        protocol ospf;
        route-filter 192.168.0.0/22 longer;
        }
        then accept;
        }
    }

Allow traffic between IS-IS and OSPF and visa versa.

    policy-statement send-direct-to-isis-neighbors {
        from {
        protocol direct;
        route-filter 10.0.0.44/30 exact;
        }
        then accept;
    }
    policy-statement send-direct-to-ospf-neighbors {
        from {
        protocol direct;
        route-filter 10.0.0.36/30 exact;
        }
        then accept;
    }
}

This is the routing instance that does only IS-IS.

routing-instances {
    buddy {
        instance-type virtual-router;
        interface ge-0/0/6.0;
        interface lo0.1;
        protocols {
        isis {
        interface ge-0/0/6.0;
        interface lo0.1;
        }
        }
    }
}

Illustration 2: Pinging the router running OSPF and getting an answer back.

Illustration 3: Pinging the virtual router buddy and getting an answer back.

The OSPF routing table contains routes to all the dummy destinations.

Illustration 4: The OSPF routing table in the redistributing router.

Connections between the routers are clearly working, looking at the routing table the OSPF system there is in fact a route that says 10.0.0.36/30 that is the network where buddy the virtual router is at.

Illustration 5: The routing table of the router running purely OSPF.
The the virtual router buddy has an IS-IS routing table that includes the network of the OSPF router 10.0.0.44/30 and the dummy routes on the loopback interface.

Illustration 6: IS-IS routing table of the redistributing router